## Slide 1
R
RCP PLATFORM · PI REVIEW
From research question to auditable simulation evidence
A practical research cockpit combining literature memory, constrained LLM reasoning, reproducible Modelica experiments, and claim-level provenance.
MODELICA × LLM-GUIDED RESEARCH × AUDITABLE EVIDENCE
17 AUGUST 2026
01

## Slide 2
CASE
The platform is a research control plane—not an autonomous scientist
It accelerates the tractable parts of computational research while making human choices and model limitations visible.
RCP.2026/11 · PI REVIEW · CASE
02
01
What it automates
Literature retrieval and screening Structured gap and hypothesis drafts Model selection and bounded parameterization Batch execution, analysis, and reporting
02
What remains human
Choice of research direction Approval of the scientific plan Interpretation of trade-offs Judgment about validity and contribution
03
What is auditable
Frozen literature snapshot Approved plan and protocol hashes Pinned runtime and raw-file fingerprints Revisioned analysis and claim links
Core proposition: move faster without collapsing generation, execution, evidence, and scientific judgment into one opaque step.

## Slide 3
CASE
Computational research is fragmented at exactly the points that matter
The costly work is not one simulation—it is preserving intent and evidence across the whole loop.
RCP.2026/11 · PI REVIEW · CASE
03
1
Literature drift
Searches change; rationales disappear; missing abstracts are easily overinterpreted.
2
Plan drift
Parameters and metrics change between the research question, execution, and analysis.
3
Environment drift
Model libraries, solvers, and runtime images silently alter behavior.
4
Evidence drift
Final prose becomes detached from cases, files, comparisons, and caveats.
The design response
Treat every transition as a typed, inspectable artifact—not just a prompt or log line.

## Slide 4
CASE
Scope is intentionally narrow: defensible simulation studies
The current domain is data-center cooling, but the control pattern is designed to generalize.
RCP.2026/11 · PI REVIEW · CASE
04
IN SCOPE
• Turn a research profile into ranked, traceable hypothesis candidates
• Compile approved ideas into registered Modelica experiments
• Execute matched studies inside a pinned OpenModelica environment
• Verify raw results, analyze under a preregistered protocol, and draft linked claims
NOT CLAIMED
• Autonomous novelty determination or publication readiness
• Physical validation without calibration data
• Universal correctness of an LLM-generated hypothesis
• Replacement for a PI, domain expert, or independent reviewer
Success means a shorter path to a reviewable study—not an automated scientific verdict.

## Slide 5
CASE
One closed loop connects intent, execution, and evidence
Eleven workflow nodes create explicit hand-offs; two human gates stop silent scientific drift.
RCP.2026/11 · PI REVIEW · CASE
Source: /api/health node graph
05
Research memory
01
Gap mining
02
Hypothesis generation
03
Select hypothesis
human gate
Compile specification
05
Approve plan
human gate
Run Modelica
07
Analyze results
08
Review evidence
09
Draft report
10
Failure handling is explicit; plan revision loops are bounded to three attempts.

## Slide 6
CASE
Four layers separate probabilistic reasoning from deterministic evidence
This boundary is the core reliability mechanism.
RCP.2026/11 · PI REVIEW · CASE
06
01
01 · RESEARCH INTERFACE
Profiles · gates · run cockpit · evidence review
02
02 · AGENT WORKFLOW
Typed state · constrained LLM calls · revision loops
03
03 · SCIENTIFIC RUNTIME
Registry · compiler · OpenModelica · batch analysis
04
04 · EVIDENCE STORE
Snapshots · raw series · hashes · revisions · exports
Boundary rule
LLMs may propose. Schemas must validate. Compilers bound. Runtimes measure. Hashes prove.
A fluent answer is never treated as a simulation result.

## Slide 7
METHOD
Constrained intelligence, not free-form automation
The LLM is useful where ambiguity is real—synthesis, framing, and drafting. Deterministic components take over where correctness can be checked.
Research Memory
Schema constraints
Human gates
Deterministic compiler
RCP.2026/11 · PI REVIEW · METHOD
07

## Slide 8
METHOD
Research Memory freezes the literature context used by the run
A reproducible snapshot makes later hypotheses and claims inspectable.
RCP.2026/11 · PI REVIEW · METHOD
08
Query planner
4 focused queries
Dual retrieval
OpenAlex + Semantic Scholar
Resolve identity
DOI deduplication
Screen
Relevance + disclosure
Enrich
Crossref metadata
Rank
Deterministic weights
Extract
PaperCards
Map
Themes + gaps
Freeze
Snapshot hash
Missing abstracts are marked insufficient; the platform does not invent methods or limitations to complete a card.

## Slide 9
METHOD
Ranking is deterministic and credibility is disclosed
Relevance dominates the score; venue status and evidence completeness remain visible rather than silently blended.
RCP.2026/11 · PI REVIEW · METHOD
09
✓
Verified
Cross-source identity and publication metadata align.
?
Likely / uncertain
Evidence is usable with an explicit confidence label.
P
Preprint
Not discarded—but never presented as peer-reviewed.
The ranking can prioritize attention; it cannot determine truth.

## Slide 10
METHOD
The LLM layer is replaceable, constrained, and measured
Current default: DeepSeek V4 Flash through an OpenRouter-compatible endpoint.
RCP.2026/11 · PI REVIEW · METHOD
Source: src/rcp/config.py and src/rcp/llm/client.py
10
0.2
Temperature
Bias toward repeatable structured outputs
JSON
Pydantic schemas
Reject malformed or incomplete responses
Retry
Validation repair
A bounded second chance—not silent coercion
Usage
Token capture
Per-call accounting retained in run state
Provider-agnostic
OpenAI-compatible client boundary allows model replacement without changing scientific artifacts.
Reasoning separated
Generated hypotheses and prose never overwrite observed Modelica outputs or hashes.
Failure visible
Provider warnings, schema failures, and missing evidence propagate to the user interface.
Model choice is a configuration decision; evidentiary rules are platform invariants.

## Slide 11
METHOD
Every task is assigned to the least ambiguous mechanism
This division of labor reduces hallucination surface and makes failures diagnosable.
RCP.2026/11 · PI REVIEW · METHOD
11
LLM-SUITABLE
DETERMINISTIC
1
Synthesize literature themes
Useful where judgment and language matter.
2
Propose research gaps
Useful where judgment and language matter.
3
Draft candidate hypotheses
Useful where judgment and language matter.
4
Explain results in plain language
Useful where judgment and language matter.
1
Resolve and rank papers
Used where the rule can be made explicit and tested.
2
Validate schemas and bounds
Used where the rule can be made explicit and tested.
3
Compile experiment cases
Used where the rule can be made explicit and tested.
4
Compute metrics, hashes, and quality gates
Used where the rule can be made explicit and tested.
Human judgment spans both columns: selecting questions, approving plans, and interpreting evidence.

## Slide 12
METHOD
Typed artifacts are the hand-offs between agents
Each stage receives a bounded object rather than an unstructured transcript.
RCP.2026/11 · PI REVIEW · METHOD
12
01
ThesisProfile
domain · interests · objectives · constraints
02
PaperCard
identity · methods · findings · limitations
03
Hypothesis
question · mechanism · contribution · risks
04
ExperimentPlan
cases · pairs · metrics · protocol
05
ResultBundle
files · fingerprints · metrics · warnings
06
Claim
statement · comparison IDs · paper IDs
Typed state makes a run resumable, testable, and reviewable without replaying the LLM conversation.

## Slide 13
METHOD
The scientific compiler turns an approved idea into executable cases
It selects only registered models and deterministically clamps or rejects unsafe parameters.
RCP.2026/11 · PI REVIEW · METHOD
13
Approved hypothesis
mechanism + boundary
Registry lookup
known model + ranges
Parameter binding
clamp / drop / warn
Plan validation
cases + matched pairs
Execution spec
sealed hash
Bounded inputs
Ranges, units, defaults, and operating envelopes live with each model.
Reproducible expansion
A 3 × 3 design becomes 18 explicit cases and nine matched pairs.
Fail closed
Unknown models, invalid structures, or unapproved plans do not reach the runtime.
Compilation is the trust boundary between generative intent and physical simulation.

## Slide 14
METHOD
Two human gates preserve scientific agency
The platform can operate quickly without treating automation as authorization.
RCP.2026/11 · PI REVIEW · METHOD
14
H1
Gate 1 · Select hypothesis
Reviewer sees ranked candidates, the research question, novelty claim, feasibility, supporting papers, risks, model fit, provider warnings, and ranking rationale.
H2
Gate 2 · Approve experiment plan
Reviewer sees the model, parameters, operating ranges, cases, matched comparisons, outputs, metrics, protocol, validation issues, and disclosures before any compute begins.
Rejecting a plan creates a visible revision request; the loop is capped at three revisions.

## Slide 15
MODELS
Modelica is the executable theory layer
Equation-based models make assumptions, state, and conservation relationships explicit—while the registry prevents ‘any model, any parameter’ execution.
OpenModelica
Model registry
Credibility tiers
Pinned libraries
RCP.2026/11 · PI REVIEW · MODELS
15

## Slide 16
MODELS
Why Modelica fits this research workflow
It supplies an inspectable physical model beneath the language-model layer.
RCP.2026/11 · PI REVIEW · MODELS
16
∑
Declarative physics
Components describe equations and connections rather than a fixed procedural solver sequence. That is valuable for multi-domain thermal and fluid systems.
↔
Composable systems
Rooms, heat exchangers, pumps, chillers, controllers, weather, and sensors can be assembled while retaining their physical interfaces.
✓
Reproducible execution
OpenModelica compiles each sealed specification inside a pinned image; outputs become files that can be fingerprinted and reanalyzed.
Modelica increases transparency of the model—but does not by itself validate the model against reality.

## Slide 17
MODELS
The model registry carries credibility and operating boundaries
Models are not interchangeable; each exposes its own inputs, outputs, validation tier, and limitations.
RCP.2026/11 · PI REVIEW · MODELS
Source: src/rcp/models_library/registry.json
17
C
DataCenterRoom
Conceptual · v1.0.0 Single-zone thermal balance with proportional cooling and constant COP. Fast enough for interactive hypothesis exploration.
N
Non-integrated plant
Library-validated · Buildings 13.0.0 Pinned wrapper around the non-integrated primary-secondary waterside-economizer example. Baseline in the milestone study.
I
Integrated plant
Library-validated · Buildings 13.0.0 Pinned wrapper around the integrated primary-secondary waterside-economizer example. Candidate configuration.
EXPLORATORY
LIBRARY REGRESSION
LIBRARY REGRESSION

## Slide 18
MODELS
DataCenterRoom is a transparent conceptual model
Its value is speed and interpretability—not facility-level fidelity.
RCP.2026/11 · PI REVIEW · MODELS
Source: DataCenterRoom.mo and model validation checks
18
ROOM ENERGY BALANCE
C · dT/dt = QIT + UA(Tamb − T) − Qcool
Qcool = clamp[kp(T − Tset), 0, Qmax]
Pcool = Qcool / COP
8 bounded parameters
0 W
energy-balance residual
26.818 °C
analytic equilibrium
100 °C
saturation branch equilibrium
bitwise
repeatability
passed
unit consistency
directional
load/capacity sensitivity
Omitted: spatial hot spots, humidity, airflow network, equipment transients, sensor uncertainty, and calibration data.

## Slide 19
MODELS
The milestone benchmark compares two Buildings library configurations
Both share the same room load, weather profile, outputs, horizon, and chilled-water setpoint.
RCP.2026/11 · PI REVIEW · MODELS
19
NON-INTEGRATED
Primary–secondary plant with waterside economizer
Load
400–600 kW
Plant
baseline
Room
return air
Separate non-integrated economizer arrangement
INTEGRATED
Primary–secondary plant with integrated economizer
Load
400–600 kW
Plant
candidate
Room
return air
Economizer integrated into the chilled-water path
Validation tier: agreement with pinned upstream library behavior—not calibration against a physical data center.

## Slide 20
MODELS
A simulation is only reproducible if its environment is named
The manifest records exact solver, libraries, image, models, inputs, code state, and artifacts.
RCP.2026/11 · PI REVIEW · MODELS
Source: data/runs/benchmark-bc0522c9/manifest.json
20
OPENMODELICA
1.26.3
MODELICA STANDARD LIBRARY
4.1.0
BUILDINGS
13.0.0
RUNTIME IMAGE
rcp-openmodelica-buildings
Reproducibility manifest also records the repository revision and dirty state—because uncommitted code is part of the environment.
Artifacts are exported as a ZIP with SHA-256 fingerprints and byte counts.

## Slide 21
STUDY
A preregistered 18-case Modelica benchmark
The study asks whether integrating a primary–secondary waterside economizer improves energy or thermal performance across load and chilled-water setpoint.
18 cases
9 matched pairs
24 h each
8 primary metrics
RCP.2026/11 · PI REVIEW · STUDY
21

## Slide 22
STUDY
The design is a complete 3 × 3 matched comparison
Every operating point runs the non-integrated baseline and integrated candidate under identical declared conditions.
RCP.2026/11 · PI REVIEW · STUDY
Source: benchmark_plan() in src/rcp/simulation/batch.py
22
6 °C CHW
8 °C CHW
10 °C CHW
400 kW
N
vs
I
N
vs
I
N
vs
I
500 kW
N
vs
I
N
vs
I
N
vs
I
600 kW
N
vs
I
N
vs
I
N
vs
I
18
simulation cases
9
matched pairs
1,440
intervals per case
N = non-integrated baseline · I = integrated candidate

## Slide 23
STUDY
The analysis protocol defines metrics before results are seen
Primary metrics, directionality, units, plausibility ranges, and quality rules are part of the approved plan.
RCP.2026/11 · PI REVIEW · STUDY
Protocol: chiller-benchmark-analysis-v2
23
EHVAC
lower
HVAC energy
kWh
PUE
lower
Power usage effectiveness
—
Tpeak
lower
Peak room temperature
°C
Exceed.
lower
Degree-hours above 27 °C
°C·h
Free
context
Free-cooling duration
h
Partial
context
Partial-mechanical duration
h
Full
context
Full-mechanical duration
h
Switches
lower
Cooling-mode transitions
count
Protocol hash 653a8df166…a997e6

## Slide 24
STUDY
A numerical impulse exposed why safeguards matter
OpenModelica trajectories contain isolated nonphysical mover-power events; raw cumulative energy is preserved, while the approved primary metric bridges screened samples.
RCP.2026/11 · PI REVIEW · STUDY
24
Physical screen
0 ≤ PHVAC ≤ 2 MW
Repair rule
Linear bridge internally; nearest valid value at a boundary.
Observed
0.068–0.512% screened
Raw upstream energy remains available as a diagnostic; it is never overwritten.

## Slide 25
STUDY
The study passes its preregistered quality gate—with one disclosed warning
Quality checks test the study artifact before any conclusion is drafted.
RCP.2026/11 · PI REVIEW · STUDY
Source: experiment_results.json quality_report
25
18 / 18
cases successful
9 / 9
matched pairs
72 / 72
comparisons
8+1
passed + warning
✓
Primary metrics complete and finite
✓
Raw-series SHA-256 integrity verified
✓
PUE remains inside 1.0–3.0
✓
Cooling-mode time balances to 24 h
✓
IT energy is monotonic with load
!
Power screening stays below 1% maximum
Quality-valid means the declared analysis is internally defensible—not that the physical model is calibrated.

## Slide 26
STUDY
Metrics remain connected to the stored trajectories
A reviewer can move from a result summary back to the screened power and room-temperature time series.
RCP.2026/11 · PI REVIEW · STUDY
26
Representative pair
500 kW · 6 °C · 24 h
Baseline
Non-integrated plant
Candidate
Integrated plant

## Slide 27
RESULTS
The integrated configuration is not an energy winner
Across all nine operating points it uses more screened HVAC energy. At 6 °C it also maintains a cooler peak room temperature—revealing a trade-off worth investigating.
+10.3% mean energy
0 / 9 energy wins
cooler at 6 °C
0 thermal exceedance
RCP.2026/11 · PI REVIEW · RESULTS
27

## Slide 28
RESULTS
Integrated HVAC energy increases in every matched pair
The increase ranges from +2.9% to +18.4%; mean change is +10.3%.
RCP.2026/11 · PI REVIEW · RESULTS
Source: benchmark revision 4b5e8132fa…27336d
28
+10.3%
mean HVAC energy
0 / 9
candidate energy wins
+2.9–18.4%
observed range

## Slide 29
RESULTS
The thermal benefit appears only at the lowest setpoint
At 6 °C, integration lowers peak room temperature by 0.243–0.869 °C; at 8–10 °C the effect is negligible or slightly adverse.
RCP.2026/11 · PI REVIEW · RESULTS
29
-0.869 °C
largest peak reduction
0 °C·h
exceedance above 27 °C
+0.105 °C
largest slight worsening

## Slide 30
RESULTS
Integration changes operating mode—not simply efficiency
At 500 kW and 6 °C, full-mechanical hours disappear, but partial-mechanical operation expands to 16.8 hours.
RCP.2026/11 · PI REVIEW · RESULTS
30
Baseline
17.1 h free + 6.9 h full
Integrated
7.2 h free + 16.8 h partial
Both
4 mode switches

## Slide 31
RESULTS
The correct conclusion is conditional—not ‘integrated is better’
The data suggest an energy–thermal-margin trade-off at 6 °C and no energy advantage elsewhere.
RCP.2026/11 · PI REVIEW · RESULTS
31
Supported
Integration can reduce peak temperature at 6 °C, with higher HVAC energy.
Not supported
Integration minimizes energy across the evaluated domain.
Next question
What control objective values thermal margin enough to justify the cost?

## Slide 32
RESULTS
Every conclusion can be traced back to a sealed chain
The same chain supports review, reanalysis, and export without trusting the narrative layer.
RCP.2026/11 · PI REVIEW · RESULTS
32
Approved plan
cc273daa59…59de99
Analysis protocol
653a8df166…a997e6
Execution specs
18 case hashes
Raw results
7a892f4093…dba500
Analysis revision
4b5e8132fa…27336d
Claim
comparison + case + paper IDs
Tamper evidence
Raw files are checked against recorded SHA-256 fingerprints before analysis.
Append-only analysis
A protocol change creates a new revision; the previous result is retained.
Claim links
Draft statements cite comparison, case, and supporting-paper identifiers.
The report is a view over evidence—not the evidence itself.

## Slide 33
RESULTS
Reanalysis is versioned instead of silently replacing history
The benchmark currently has two stored analysis revisions; the newest records that the protocol changed.
RCP.2026/11 · PI REVIEW · RESULTS
33
REVISION 01
f906…ec70f
Retained as historical analysis
protocol change
CURRENT
4b5e8132fa…27336d
Metrics recomputed from stored raw series
Result: methodological improvement without erasing the record that supported earlier outputs.

## Slide 34
PRODUCT
The interface is designed around reviewable research state
Light and dark themes, keyboard-visible controls, responsive layouts, URL-addressable views, and explicit lifecycle actions are now implemented.
RCP.2026/11 · PI REVIEW · PRODUCT
34
RUN PORTFOLIO
RUN COCKPIT
Status at a glance
Active, attention, completed, and failed runs remain visible.
Lifecycle navigation
Stages, gates, tabs, claims, and artifacts are one click away.
Safe operations
Archive and retry update the same view after the backend succeeds.

## Slide 35
PRODUCT
Researchers can move from profile to literature to simulation
The UI exposes the same boundaries as the scientific workflow rather than hiding them behind a chat box.
RCP.2026/11 · PI REVIEW · PRODUCT
35
01 · Frame
Research profile + constraints
02 · Ground
Credibility-aware PaperCards
03 · Explore
Bounded model quick simulation

## Slide 36
PRODUCT
Reviewers reach the platform over an authenticated link
One supervised process on loopback, an outbound TLS tunnel, and HTTP Basic auth covering the API, the SPA, and the live run stream alike.
RCP.2026/11 · PI REVIEW · PRODUCT
Source: docs/DEPLOYMENT.md · deploy/rcp.service · src/rcp/api/auth.py
36
Reviewer browser
nothing to install
Tailscale Funnel
public TLS · 443
Basic auth gate
ASGI middleware
Supervised rcp serve
127.0.0.1 · systemd
Run manager
one worker · Docker
Fail closed by default
`rcp serve` will not start without a password, will not accept one under 16 characters, and will not disable auth on a non-loopback host.
Nothing streamed was broken
A pass-through gate, not a response wrapper: run events keep flowing (with a 15 s keepalive for proxy idle timeouts) and PDF range requests still return 206.
Supervised, single worker
A systemd unit with a 120 s stop timeout for the 1200 s simulation call. Live run state is in-process, so a worker count is structurally refused.
What it protects
Anonymous access to the API, the interface, the event stream, and the schema — the interactive docs are withdrawn whenever auth is on.
What it is not
One shared credential identifies nobody, rate-limits nothing, and caps no spend. The Funnel hostname is published to Certificate Transparency logs.
The credential is transport protection, not evidence of who did what—so exposure stays temporary and `reviewer_id` stays self-declared.

## Slide 37
PRODUCT
Evaluation separates software correctness from scientific validity
Passing tests proves the platform behaves as declared; it does not prove a model represents a facility.
RCP.2026/11 · PI REVIEW · PRODUCT
Source: docs/EVALUATION.md
37
A
Automated verification
Backend tests Frontend interaction tests Production build Environment doctor Model validation checks Raw integrity + study quality
N
Numerical regression
Pinned upstream trajectories Normalized RMSE threshold ≤ 0.5% Benchmark repeatability Metric completeness Physical plausibility screens
H
Manual blind review
Traceability Missing-evidence visibility Preregistration Reproducibility Calibration disclosure Verification time
Manual review uses at least two reviewers and never collapses into a single ‘scientific validity score.’

## Slide 38
PRODUCT
Current state: a tested research prototype with a credible benchmark
The platform is ready for guided research use and PI scrutiny—not unsupervised scientific deployment.
RCP.2026/11 · PI REVIEW · PRODUCT
38
174
backend tests passed
60
frontend tests passed
7 / 7
conceptual model checks
valid
18-case study quality
Strong today
Auditable workflow, bounded registry, pinned runtime, evidence hashes, revisioned analysis, coherent UI, and a supervised authenticated deployment.
Needs research work
Facility calibration, uncertainty quantification, broader scenarios, and independent replication.
Needs product work
Per-reviewer identity, rate limiting and spend caps, multi-user provenance, long-running job infrastructure, and observability.
Readiness claim: strong prototype for supervised, reproducible computational studies.

## Slide 39
NEXT
The largest risks are scientific, not cosmetic
Each risk has a concrete mitigation path; none should be hidden by a polished interface.
RCP.2026/11 · PI REVIEW · NEXT
39
Calibration gap
Library regression is not facility validation.
MITIGATION
Acquire measured plant data; calibrate and hold out validation periods.
Scenario narrowness
One dry-cold weather profile and a 3 × 3 operating matrix.
MITIGATION
Add climates, seasons, load profiles, faults, and control variants.
LLM dependence
Hypothesis quality varies with model and retrieval coverage.
MITIGATION
Benchmark prompts/models; capture uncertainty; retain human selection.
Numerical events
Isolated mover-power impulses require a declared screen.
MITIGATION
Investigate upstream dynamics and compare alternate solvers/tolerances.
The platform makes these limitations easier to see; resolving them remains research work.

## Slide 40
NEXT
The next phase should deepen evidence before broadening automation
A staged roadmap keeps scientific credibility ahead of product surface area.
RCP.2026/11 · PI REVIEW · NEXT
40
0–3 months
VALIDATE
Replicate benchmark Investigate power impulses Add uncertainty bands Define calibration dataset
3–6 months
GENERALIZE
New weather profiles Dynamic load traces Control variants Cross-solver comparison
6–12 months
TRANSLATE
Facility calibration Prospective case study Independent reviewer study Operational deployment plan
Decision rule: do not add a new autonomous step until its inputs, outputs, failure modes, and review point are explicit.

## Slide 41
PI DISCUSSION
Three decisions unlock the next research phase
01
Scientific target
Optimize energy only—or formalize a weighted energy / thermal-margin objective?
02
Validation access
Which facility data, collaborator, or measured benchmark can anchor calibration?
03
Evaluation design
Which users and reviewers should test traceability and verification-time gains?
Take-away
RCP can make simulation research faster and more reviewable—provided the model, protocol, and human judgment remain first-class evidence.
RCP.2026/11 · 17 AUGUST 2026
41